## Slide 1: Stopping distances for cars

## Slide 2
Built up area

## Slide 3
Built up area

## Slide 4
Single carriageway

## Slide 5
Dual carriageway

## Slide 6
Motorway

## Slide 7
Different types of roads have different speed limits.
Why do you think this is?

## Slide 8: Lesson objective: know your stopping distances
Lesson outcomes:
State what is the meaning of braking distance, thinking distance and stopping distance.
Describe what can affect the braking distance, thinking distance and stopping distance.
Explain – using forces, how the affect increases the braking distance, thinking distance and stopping distance.

## Slide 10: Would you like a car?

## Slide 11: Visit nice places

## Slide 12: Well, you need to pass your test first! A written exam and a practical exam

## Slide 13: Stopping distances


Thinking distance is the distance a car travels before the brakes are applied.
Braking distance is the distance a car travels whilst the brakes are being applied.
Stopping distance = thinking distance + braking distance
Stopping distance
Braking distance
Thinking distance
How long does it take a moving vehicle to stop?
The stopping distance is the sum of the thinking distance and the braking distance.

## Slide 14: Braking distance
The distance the car travels during its deceleration, whilst the brakes are being applied
The distance the car travels in the split second between a hazard appearing and the driver applying the brakes
Thinking distance

## Slide 15
The total stopping distance = thinking distance + breaking distance
30mph
9m +
14m = 6 car lengths
50mph
15m + 38m = 13 car lengths
70mph
21m + 75m = 24 car lengths

## Slide 16: Thinking distance
It is affected by 3 main things:
How fast you are going
Being wide awake – drugs, tiredness, alcohol, carelessness and old age.
Visibility – rain, oncoming lights, fog and the night.

## Slide 19: Braking distance
It is affected by 4 main factors:
How fast you are going
The mass (or load) of the vehicle
If the car is poorly maintained – brakes and tyres (groves in tyres – 1.6mm deep)
The grip of the road surface – on a wet road you can skid twice as long

## Slide 20: What about braking?
If friction is absent during braking, the wheels will lock – they will stop turning.
This is very dangerous – mainly because the car will slide, but also because the car cannot be steered.
Forces

## Slide 21: Can you match up the words with their definitions?
Stopping distance
Friction
Thinking distance
Braking distance
One of forces the road exerts on the tyres as the car is stopping.
The distance a car travels whilst it is braking.
The distance a car travels before the brakes are applied.
The sum of thinking distance and the braking distance.

## Slide 22: What factors affect braking and thinking distance?
Thinking distance | Braking distance
Speed of car
Speed of car
Speed of car
Road conditions
Road conditions
Drugs and alcohol
Drugs and alcohol
Tiredness
Tiredness
Medication
Medication
Condition of tyres
Condition of tyres
Condition of brakes
Condition of brakes

## Slide 23
What effects the thinking distance?
What effects the braking distance?
Why do bald
tyres increase
the stopping
distance
of a car?

## Slide 24: Stopping a car…
Braking distance
Too much alcohol
Thinking distance
Tiredness
Too many drugs
Wet roads
Driving too fast
Tyres/brakes worn out
Icy roads
Poor visibility

## Slide 25: Why can an icy road increase the stopping distance of a car?
The is little friction between the road and your tyres. Forces are unbalanced and you will keep going forward.

## Slide 26: What could you do to prevent skidding into another car?
Reduce your speed

## Slide 27: Why do bald tyres increase the stopping distance of a car?
The is little friction between the road and your tyres. Forces are unbalanced and you will keep going forward.

## Slide 28: Braking car question:
A car is moving along an open road. Suddenly, a sheep walks into the road.
What do we call the distance the car travels before the driver puts their foot on the brakes?
Name one factor that could increase the distance the car travels in this time.
Thinking distance
Medication, drugs/alcohol, speed of car, tiredness

## Slide 29: Braking car question:
A car is moving along an open road. Suddenly, a sheep walks into the road.
What do we call the distance the car travels before the driver puts their foot on the brakes?
Name one factor that could increase the distance the car travels in this time.

## Slide 30: Braking car question:
A car is moving along an open road. Suddenly, a sheep walks into the road.
What do we call the distance the car travels before the driver puts their foot on the brakes?
Name one factor that could increase the distance the car travels in this time.

## Slide 31: Speed kills
What other measures are taken to stop motorists from speeding?

## Slide 32: Thinking distance
The distance the car travels in the split second between a hazard appearing and the driver applying the brakes
Reaction timer
You can test your reactions by holding the top of a 30cm ruler, hanging vertically between a partners finger and thumb.
When you let go (no warning) your partner has to grip the ruler as quickly as possible.
The slower your partner's reaction time the further the ruler will fall or use a reaction timer on the computer.